DORMA-Glas Sliding door shower fittings series ATNEO S1

Designation: ATENO S1
Design: Sliding door shower fitting series with soft-closing and retractable function
Manufacturer: DORMA-Glas GmbH

PRODUCT DESCRIPTION / FUNCTIONS
Sliding door shower fitting series with soft-closing and retractable function on both sides,
pre-assembled and concealed functional elements, infinitely adjustable damper function,
Sliding door easy to hang, height adjustment +/- 3 mm,
lateral adjustment in the profile -10 mm, divisible magnetic floor guide for easy cleaning
between the glass elements, corner showers fully or partially framed, wall and ceiling mounting

TECHNICAL FEATURES
- Material: aluminum
- Surfaces:
   Standard surfaces: polished chrome, p-coated deep black matte
   Special finishes: p-coated RAL xxxx
- Glass type: TSG (EN 12150-1)
- Glass thickness: 8 mm / 10 mm
- Max. door leaf weight: 50 kg
- Min. door leaf width: 400 mm
- Max. door leaf width: depending on installation situation (see planning manual)
- Max. system height with/without vertical wall connection profile:
   Wall mounting: 2,568 mm/3,000 mm
   Ceiling mounting: 2,576 mm/3,000 mm
- Sliding profile W 56 x H 69 mm / max. length: 2,800 mm
- Gap dimensions between the glass elements: 12 mm
- Self-adhesive handle bar with mounting template
  (Alternative: sliding door knob with 12 mm hole)
- No glass preparation (if self-adhesive handle bar is used)
- Height adjustment (+3/-3 mm) / lateral adjustment in profile -10 mm
- Damping and retraction function on both sides (from 400 mm door leaf width)

APPROVAL AND CERTIFICATES
- tested in accordance with DIN EN 14428:2019-07

AREAS OF APPLICATION
- 1-2 leaf shower systems with side panels
- for niche, corner, U-shaped, bathtub and walk-in showers

PRODUCT DESIGN
ATENO S1 system types – wall mounting
Complete sets consisting of: sliding profile,
clip and cover profiles, wall connection profile,
clamping and slide unit, damper unit, starter, floor guide,
handle bar, all sealing profiles:
- Niche shower type 1: W '..........' x H '..........'  piece '..........'
- Niche shower type 2: W '..........' x H '..........'  pieces '..........'
- Niche shower type 3: W '..........' x H '..........'  pieces '..........'
- Corner shower type 4: W '..........' x W '..........' x H '..........'  pieces '..........'
- Corner shower type 5: W '..........' x W '..........' x H '..........'  units '..........'
- Corner shower type 6: W '..........' x W '..........' x H '..........'  pieces '..........'
- Corner shower type 7: W '..........' x W '..........' x H '..........'  pieces '..........'
- U-shaped shower type 8: W '..........' x W '..........' x W '..........' x H '..........'  Units '..........'
- Walk-in shower type 9: W '..........' x H '..........'  pieces '..........'

ATENO S1 system types – ceiling mounting
Complete sets consisting of: sliding profile, adapter profile,
clip and cover profiles, wall connection profile,
clamping and slide unit, damper unit, starter, floor guide,
handle bar, all sealing profiles:
- Niche shower type 1: W '..........' x H '..........'  piece '..........'
- Niche shower type 2: W '..........' x H '..........'  pieces '..........'
- Niche shower type 3: W '..........' x H '..........'  pieces '..........'
- Corner shower type 4: W '..........' x W '..........' x H '..........'  pieces '..........'
- Corner shower type 5: W '..........' x W '..........' x H '..........'  units '..........'
- Corner shower type 6: W '..........' x W '..........' x H '..........'  pieces '..........'
- Corner shower type 7: W '..........' x W '..........' x H '..........'  pieces '..........'
- U-shaped shower type 8: W '..........' x W '..........' x W '..........' x H '..........'  Units '..........'
- Walk-in shower type 9: W '..........' x H '..........'  pieces '..........'

ATENO S1 system types – wall mounting, partially framed,
Complete sets consisting of: sliding profile incl. cover cap only
on door leaf level, clip and cover profiles, wall connection profile,
clamping and slide unit, damper unit, starter, floor guide,
handle strip, all sealing profiles:
- Corner shower type 4: W '..........' x W '..........' x H '..........'  piece '..........'
- Corner shower type 5: W '..........' x W '..........' x H '..........'  pieces '..........'
- Corner shower type 7: W '..........' x W '..........' x H '..........'  piece '..........'

DOOR TYPE
Sliding glass door and glass side panels

MOUNTING POSITION
Wall mounting, ceiling mounting

SURFACES (standard)
- polished chrome (F119) '..........'
- powder-coated, deep black, smooth, matt, RAL 9005 (F304) '..........'

SURFACES (special)  on request
- powder-coated, RAL xxxx (F399) '..........'

ACCESSORIES
- self-adhesive handle strip with mounting template '..........'
- door knob with 12 mm hole '..........'