DORMA-Glas Single-action door shower hinge series TANORA S1

Designation: TANORA S1
Design: Single-action door shower hinge series
Manufacturer: DORMA-Glas GmbH

PRODUCT DESCRIPTION / FUNCTIONS
Door fittings opening 90° on one side, Cover caps for invisible screws,
wall mounting with elongated holes,
Matching fixed part fittings and connectors

TECHNICAL FEATURES
- Material: Brass
- Surfaces:
   Standard surfaces: polished chrome, sim. stainless steel matte, p-coat. black matte
   Special surfaces: p-coat. RAL xxxx, elektroplating
- Glass type: TSG (EN 12150-1)
- Glass thickness: 8 mm
- Glass mounting: with clamping plate
- Max. load capacity (2 hinges): 40 kg
- Max. door width: 1000 mm
- also for folding doors
- also for sauna cabins (till 90°C)
- Durability test inhouse according to DIN EN 14428:2019-07

AREAS OF APPLICATION
1/2-leaf showers, partly with fixed and/or side panel

PRODUCT ASSORTMENT
- Hinge glass-wall '..........'
- Hinge glass-glass 180° '..........'
- Bracket glass-wall 90° '..........'
- Bracket glass-glass 90° '..........'
- Connector glass-wall 180° '..........'
- Connector glass-glass 180° '..........'
SURFACES (Standard)
- polished chrome (F501) '..........'
- sim. stainless steel matte (F507) '..........'
- powder coated, deep black, smooth, matte, RAL 9005 (F504) '..........'
SURFACES (Special)  auf on request
- powder coated, RAL xxxx (F599) '..........'
- elektroplating (e.g. copper brushed, brass matt brushed …) '..........'

GLASS
- TSG 8 mm '..........'

ACCESSORIES
- Door handle L-form - f. 8 mm glass '..........'
- Door knob square - f. 8 mm / 10 mm / 12 mm '..........'